## Slide 1: Littelfuse SP33R6-04UTG: 12kV TVS Diode Array for Ultra High Speed Interfaces
Americas Components

## Slide 2
The new SP33R6 is a series of four-channel, low capacitance (0.2pF) TVS diode arrays. These robust diodes provide extremely low breakdown/turn-on voltages, making them ideal protectors of high-speed data lines with low voltage (-0.3 to +0.3V).
Without performance degradation, they can safely absorb repetitive ESD strikes above the maximum level specified in IEC 61000-4-2 international standard (Level 4, ±8kV contact discharge).
Low capacitance of 0.2pF (TYP) per I/O
ESD, IEC 61000-4-2, ±12kV contact, ±15kV air
EFT, IEC 61000-4-4, 40A (5/50ns)
Lightning, 3A (8/20μs as defined in IEC 61000-4-5, 2nd Edition)
Halogen free, lead free and RoHS compliant
FEATURES
BENEFITS
OVERVIEW
Compliant with numerous IEC standards for ESD suppression and lightning surge protection
Four channels with low capacitance to protect ultra-high-speed interfaces
An environmentally friendly component that is halogen-free, lead-free, and RoHS compliant.

## Slide 3
ESD Withstand Voltage (Contact) ±12kV
ESD Withstand Voltage (Air) ±15kV
Line Capacitance (f=3GHz) 0.2pF
Peak Current (tp=8/20μs) 3A
Reverse Standoff Voltage (IR=1uA) 0.3V
Breakdown Voltage (IR=1mA) 0.6V to 0.9V
Reverse Leakage Current (VR=0.3V) 100nA
Clamp Voltage (IPP=1A, TP=8/20us) 2.5V
Clamp Voltage (IPP=2A, TP=8/20us) 3.3V
Dynamic Resistance (tp=100ns) 0.3Ohms
Operating Temperature -40°C to 125°C
TARGET MARKETS & APPLICATIONS
MECHANICAL & ELECTRICAL PERFORMANCE
Datasheet: Link
Provides exceptional protection for electronics used in appliances, building automation, outdoor lighting, and smart meter applications.
Ideal for: USB 3.2, USB 4.0, Thunderbolt 3.0, PCIE
Part Number | Description | Package
SP33R6-04UTG | 0.2pF, 12kV, 0.6V | μDFN-10